## Slide 1
Design an eight bit down counter by using 4-bit programmable down counters with load. This counter will have a control input CNT. The designed 8-bit down counter will count when the CNT input is 1, this counter will repeat the whole process until CNT=0. (use the counter symbol given below in your solution, you may use extra logic.)

## Slide 2: Introduction
Chpt 2
  Capture Comb. behavior: Equations, truth tables
  Convert to circuit: AND + OR + NOT  Comb. logic
Chpt 3
  Capture sequential behavior: FSMs
  Convert to circuit: Register + Comb. logic  Controller
Chpt 4
  Datapath components, simple datapaths
Chpt 5
  Capture behavior: High-level state machine
  Convert to circuit: Controller + Datapath  Processor
  Known as “RTL” (register-transfer level) design
Note: Slides with animation are denoted with a small red "a" near the animated items
T
r
ansistor l
e
v
el
Logic l
e
v
el
Register-
t
r
ans
f
er
l
e
v
el (
R
TL)
Levels of digital design abstraction
Higher levels
Processors:
  Programmable (microprocessor)
  Custom
5.1

## Slide 3: FSM summary
Identify the inputs and outputs
Sketch the state transition diagram (analyze behaviour)
Write state transition table
Write output table
  Write combined state transition table + output table (for mealy FSM)
Select state encoding
Write boolean equations for next state and output logic
Sketch the circuit schematic

## Slide 4
Register Transfer Level (RTL)
Combinational behaviour-boolean equations or truth tables (implemented as a circuit of gates)
Sequential behaviour-finite state machines (implemented as a circuit having combinational logic and register)
Transistor Level
Logic Level
Register Transfer Level
Transistors are connected to build gates or other components
Designing combinational or sequential circuits whose building blocks are logic gates
Processors are designed using circuits which consist of registers and datapath components.
Data is transferred in between registers through datapath. Such design is called register transfer level (RTL) design

## Slide 5
Register Transfer Level (RTL)
Microprocessor?
Processors are designed using circuits which consist of registers and datapath components.
Data is transferred in between registers through datapath. Such design is called register transfer level (RTL) design
Programmable processor which is a general processor to carry out any desired computation.
Can design custom processors which are specialized to implement one specific computation. (look like functions in the code)
Custom processors can be small, low-power and fast.
The RTL design process has two main sections
  Capture behaviour (by using High Level State Machine (HLSM))
  Convert to circuit

## Slide 6: High-Level State Machines (HLSMs)
Some behaviors too complex for equations, truth tables, or FSMs
Ex: Soda dispenser
  c: bit input, 1 when coin deposited
  a: 8-bit input having value of deposited coin
  s: 8-bit input having cost of a soda
  d: bit output, processor sets to 1 when total value of deposited coins equals or exceeds cost of a soda
FSM can’t represent…
  8-bit input/output
  Storage of current total
  Addition (e.g., 25 + 10)
a
s
c
d
Soda
dispenser
processor
25
1
0
25
1
1
50
0
0
0
0
tot:
25
tot:
50
a
s
c
d
Soda
dispenser
processor
5.2

## Slide 7: HLSMs
High-level state machine (HLSM) extends FSM with:
  Multi-bit input/output
  Local storage
  Arithmetic operations (like add, compare)
Inputs:
c
(bit),
a (8 bits), s (8 bits)
Outputs:
d (bit) // '1' dispenses soda
Local stor
a
g
e
:
tot (8 bits)
W
ait
Disp
Init
d:='0'
tot:=0
c’*(tot<s)’
c'
*
(
tot<s
)
d:='1'
c
tot:=tot+a
SodaDispenser
8
8
a
s
c
d
Soda
dispenser
processor
Conventions
  Numbers:
    Single-bit: '0' (single quotes)
    Integer: 0 (no quotes)
    Multi-bit: “0000” (double quotes)
  == for equal, := for assignment
  Multi-bit outputs must be registered via local storage
  // precedes a comment
a
Add

## Slide 8
High-Level State Machines (HLSMs)
A FSM is not sufficient for capturing this system’s behaviour
FSM can have single bit inputs and outputs.
No way of keeping track of the total value of coins deposited
FSM can only perform boolean operations (not data addition)
HLSM extends FSM by;
  Multibit data inputs and outputs
  Local storage
  Arithmetic operations (addition, comparasion etc.)

## Slide 9
High-Level State Machines (HLSMs)
The state machine is not a FSM because it has 8-bit input and it declares local storage tot to store intermediate data.
State actions and state transition conditions involve data operations like addition, not OR, comparison etc.
Conventions
  Each transition is impicitly ANDed with a rising clock edge
  Any bit output not assigned a value in a state is implicitly assigned to 0 (not applied for multibit outputs)
  Single quotes: bit values like ‘0’, ‘1’
  Double quotes: multibit values like “000011”

## Slide 10
High-Level State Machines (HLSMs)
Conventions (Cnt’d)
  Multibit storage items can be assigned the numbers 0,1,2...
  == comparison
  := assignment
  Every multibit output is registered Every multibit output X must have a storage item Xreg which has the same width as X.
  If a single-bit output B is used, can be registered by declaring item Breg.
  Can include text for explanations. Comments are preceded by //

## Slide 11
Example
Capture a HLSM for a system having an input m (1 bit) and 32 bit output P. The system should output the total number of clock cycles for which the input m is 1.
Inputs: m (bit)
Outputs: P (32 bits)
Local Storage: Preg

## Slide 12: Ex: Cycles-High Counter
P = total number (in binary) of cycles that m is 1
Capture behavior as HLSM
  Preg required (multibit outputs must be registered)
    Use to hold count
P
m
CountHigh
clk
32
S_Clr
S_Wt
m'
S_Inc
m
m
m'
Preg := 0
Preg := Preg + 1
// Clear Preg to 0s
// Wait for m == '1'
// Increment Preg
CountHigh
Inputs
:
m
(bit)
Outputs
:
P (32 bits)
Local storage:
Preg
(c)
S_Clr
Preg := 0
// Clear Preg to 0s
CountHigh
Inputs
:
m
(bit)
Outputs
:
P (32 bits)
Local storage:
Preg
(a)
?
S_Clr
S_Wt
m'
m
Preg := 0
// Clear Preg to 0s
// Wait for m == '1'
CountHigh
Inputs
:
m
(bit)
Outputs
:
P (32 bits)
Local storage:
Preg
(b)
?
a
Note: Could have designed directly using an up-counter. But, that methodology is ad hoc, and won't work for more complex examples, like the next one.
a
Preg

## Slide 13: Example: Laser-Based Distance Measurer
Laser-based distance measurement – pulse laser, measure time T to sense reflection
  Laser light travels at speed of light, 3*108 m/sec
  Distance is thus D = (T sec * 3*108 m/sec) / 2
Object of
interest
D
2D = T sec * 3*108 m/sec
sensor
laser
T (in seconds)
a

## Slide 14
Example-Laser-Based Distance Measurer
In laser-based distance measurement, a laser is pointed at the object of interest. The laser pulse is briefly turned on and a timer is started. The laser travels to the object and reflects back. A sensor detects the reflection of the laser (ToDoA). If we know the travel time T of the laser we can calculate the distance by using the speed of light.
Input: B (1 bit) – button to start the measurement
Input: s (1 bit) – reflected laser beam detected.
Output: L (1 bit) – Turn on laser source
Output: D (16 bit) – Distance measured in binary
Local Storage: Clock Count
Laser-based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor

## Slide 15
Laser-Based Distance Measurer
Sequencce
  System is powered ON. Distance is reset to 0.
  System waits for the button input B
  Once the button is pressed system turns on laser
  After laser is turned on system waits for the reflected laser beam. Meanwhile the clock cycles are counted.
  After the reflected laser is sensed distance is calculated by the clock count
  System returns back to the state where it waits for button input.

## Slide 16: Example: Laser-Based Distance Measurer
Inputs/outputs
  B: bit input, from button, to begin measurement
  L: bit output, activates laser
  S: bit input, senses laser reflection
  D: 16-bit output, to display computed distance
sensor
laser
T (in seconds)
Laser-based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor

## Slide 17: Example: Laser-Based Distance Measurer
Declare inputs, outputs, and local storage
  Dreg required for multi-bit output
Create initial state, name it S0
  Initialize laser to off (L:='0')
  Initialize displayed distance to 0 (Dreg:=0)
Laser-
based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor
a
Inputs
:
B (bit), S (bit)
Outputs
:
L (bit), D (16 bits)
Local storage:
Dreg(16)
S0
?
L
:= '0' //
laser off
Dreg := 0 //
distance is 0
DistanceMeasurer
(required)
(first state usually initializes the system)
Recall: '0' means single bit, 0 means integer

## Slide 18: Example: Laser-Based Distance Measurer
Add another state, S1, that waits for a button press
  B' – stay in S1, keep waiting
  B – go to a new state S2
Q: What should S2 do?
A: Turn on the laser
a
Laser-
based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor
S0
L := '0'
Dreg := 0
S1
?
B'
// button not pressed
B
// button
pressed
S0
DistanceMeasurer
...

## Slide 19: Example: Laser-Based Distance Measurer
Add a state S2 that turns on the laser (L:='1')
Then turn off laser (L:='0') in a state S3
Q: What do next?
A: Start timer, wait to sense reflection
a
Laser-
based
distance
measurer
16
from button
to display
S
L
D
B
to laser
from sensor
DistanceMeasurer
...
S0
S1
L := '0'
Dreg := 0
S2
L := '1'
// laser on
S3
L := '0'
// laser off
B'
B

## Slide 20: Example: Laser-Based Distance Measurer
Stay in S3 until sense reflection (S)
To measure time, count cycles while in S3
  To count, declare local storage Dctr
  Initialize Dctr to 0 in S1. In S2 would have been O.K. too.
    Don't forget to initialize local storage—common mistake
  Increment Dctr each cycle in S3
Laser-based
distance
measurer
16
f
r
om button
t
o display
S
L
D
B
t
o laser
f
r
om sensor
a
S0
S1
S2
S3
L := '0'
Dreg := 0
L := '1'
L := '0'
Dctr := Dctr + 1
// count cycles
Dctr := 0
// reset cycle
count
B'
S'
// no reflection
B
S
//
reflection
?
Inputs
:
B (bit), S (bit)
Outputs
:
L (bit), D (16 bits)
Local storage:
Dreg,
Dctr (16 bits)
DistanceMeasurer

## Slide 21: Example: Laser-Based Distance Measurer
Once reflection detected (S), go to new state S4
  Calculate distance
  Assuming clock frequency is 3x108, Dctr holds number of meters, so Dreg:=Dctr/2
After S4, go back to S1 to wait for button again
a
S0
S1
S2
S3
L := '0'
Dreg := 0
L := '1'
L := '0'
Dctr := Dctr+1
Dreg := Dctr/2
// calculate D
Dctr := 0
B'
S'
B
S
S4
Inputs
:
B (bit), S (bit)
Outputs
:
L (bit), D (16 bits)
DistanceMeasurer
Local storage:
Dreg, Dctr (16 bits)
Laser-based
distance
measurer
16
from button
to display
S
L
D
B
t
o laser
from sensor

## Slide 22: HLSM Actions: Updates Occur Next Clock Cycle
Local storage updated on clock edges only
  Enter state on clock edge
  Storage writes in that state occur on next clock edge
  Can think of as occurring on outgoing transitions
Thus, transition conditions use the OLD value, not the newly-written value
  Example:
S3
Dctr := Dctr+1
S'
S
S3
Dctr := Dctr+1
S' /
S /
Dctr := Dctr+1
S0
S1
P := '1'
Jreg := Jreg + 1
P := '0'
Jreg := 1
B'
B
Inputs
:
B (bit)
Outputs
:
P (bit) // if B, 2 cycles high
Local storage:
Jreg (8 bits)
!(Jreg<2)
Jreg<2
?
1
S0
1
2
S1
2
S1
clk
clk
Jreg
B
S0
P
3
(
a
)
(
b
)
3

## Slide 23
Example: Cycles High Counter
Capture a HLSM for a system having an input m (1 bit) and 32 bit output P. The system should output the total number of clock cycles for which the input m is 1.
Inputs: m (bit)
Outputs: P (32 bits)
Local Storage: Preg

## Slide 24
Example: Cycles High Counter
Cycles High Counter Example
  Clear Preg
  Increment Preg for each CLK cycle that m is 1.
We must design the controller to generate preg_clr and preg_ld signals. For this purpose;
  Carry the register and arithmetic oprations on the datapath
  Convert the HLSM to a FSM for the controller part
P
Preg
m
CountHigh
Preg
Q
I
ld
clr
A
B
S
add1
P
000...00001
?
Preg_clr
Preg_ld
m
DP
CountHigh
(c)
32
32
S_Clr
S_Wt
m'
S_Inc
m
m
m'
Preg := 0
Preg := Preg + 1
// Clear Preg to 0s
// Wait for m == '1'
// Increment Preg
CountHigh
Inputs
:
m
(bit)
Outputs
:
P (32 bits)
Local storage:
Preg

## Slide 25: FSM summary
Identify the inputs and outputs
Sketch the state transition diagram
Write state transition table
Write output table
  Write combined state transition table + output table (for mealy FSM)
Select state encoding
Write boolean equations for next state and output logic
Sketch the circuit schematic

## Slide 26
Cycles High Counter Example
We can implement controller FSM by using a register and combinational logic
  Write state transition table and output table using binary encoding
  Write binary equations for next state and output
  Draw the circuit schematic
S_Clr
S_Wt
m'
S_Inc
m
m
m'
Preg_clr = 1
Preg_ld = 0
Preg_clr = 0
Preg_ld = 0
Preg_clr = 0
Preg_ld = 1
(d)
//Preg := 0
//Wait for m=1
//Preg:=Preg+1
Controller
CountHigh
P
Preg
Q
I
ld
clr
A
B
S
add1
000...00001
Preg_clr
Preg_ld
DP
m
32
32
State | Current State |  | Input | Next State | 
 | S1 | S0 | M | S1’ | S0’
S0 | 0 | 0 | X | 0 | 1
S1 | 0 | 1 | 0 | 0 | 1
S1 | 0 | 1 | 1 | 1 | 0
S2 | 1 | 0 | 0 | 0 | 1
S2 | 1 | 0 | 1 | 1 | 0
Encoding |  |  | State | Outputs | 
 |  |  |  | Preg_clr | Preg_ld
 | S1 | S0 |  |  | 
S0 | 0 | 0 | S_clr | 1 | 0
S1 | 0 | 1 | S_wt | 0 | 0
S2 | 1 | 0 | S_Inc | 0 | 1
S1’=(S1+S0)M
S0’=+
Preg_clr =
Preg_ld=S1
Next state – output logic functions

## Slide 27
Cycles High Counter Example
S1’=(S1+S0)M
S0’=+
Preg_clr =
Preg_ld=S1

## Slide 28: Ctrl/DP Example for Earlier Cycles-High Counter
(a)
First clear Preg to 0s
Then increment Preg for each
clock cycle that m is 1
P
Preg
m
CountHigh
(b)
S_Clr
S_Wt
m'
S_Inc
m
m
m'
Preg := 0
Preg := Preg + 1
//Clear Preg to 0s
//Wait for m=='1'
//Increment Preg
CountHigh
Inputs
:
m
(bit)
Outputs
:
P (32 bits)
LocStr
: Preg (32 bits)
Preg
Q
I
ld
clr
A
B
S
add1
P
000...00001
?
Preg_clr
Preg_ld
m
DP
CountHigh
(c)
32
32
S_Clr
S_Wt
m'
S_Inc
m
m
m'
Preg_clr = 1
Preg_ld = 0
Preg_clr = 0
Preg_ld = 0
Preg_clr = 0
Preg_ld = 1
(d)
//Preg := 0
//Wait for m=1
//Preg:=Preg+1
Controller
CountHigh
P
Preg
Q
I
ld
clr
A
B
S
add1
000...00001
Preg_clr
Preg_ld
DP
m
32
32
We created this HLSM earlier
Create DP
Connect with controller
Derive controller
a
a
a

## Slide 29
High-Level State Machines (HLSMs)
  Multibit data inputs and outputs
  Local storage
  Arithmetic operations (addition, comparasion etc.)
RTL Design Process
  Capture the behaviour using a HLSM
  Convert HLSM to a circuit
    Capture a high-level state machine
    Create a datapath
    Connect the datapath to a controller
    Derive the controller's FSM

## Slide 30
RTL Design Process
RTL design follows two-step process
  Capture the behaviour using a HLSM
  Convert HLSM to a circuit
HLSM is converted to a circuit by using standard processor architecture
External data
outputs
External
control
inputs
Controller
...
External
control
outputs
...
Datapath
...
DP
control
inputs
DP
control
outputs
...
...
...
External data
inputs
Data path has the ability to carry out each data operation in HLSM
Controller sets the control signals for data path components for performing specific actions of each state and to transition to next states

## Slide 31
High-Level State Machines (HLSMs)
RTL Design Process
  Capture the behaviour using a HLSM
  Convert HLSM to a circuit
    Capture a high-level state machine
    Create a datapath
    Connect the datapath to a controller
    Derive the controller's FSM
Controller-Datapath

## Slide 32: RTL Design Process

## Slide 33
Creating Datapath
Make all data inputs and outputs to be datapath inputs and outputs
Instantiate (add) a register into the datapath for every local storage item in HLSM
Examine each state action and each transition condition for data computations
Connect components to implement each data computation
Add multiplexers in front of component inputs if necessary
Instance: Instantiated componenet – new component. Give a unique, meaningful name for each component (Reg1, Reg2, TemperatureReg, SensorReg etc.)
A library can be used for component selection during datapath design.

## Slide 34
Creating Datapath
When instantiating a new component for datapath in HLSM all control inputs (like clr, ld, etc.) must be introduced externally.
Unique names must be given to each new component (similar to naming variables in C) such as (Preg_clr, Preg_ld, RegQ_clr, RegQ_ld etc.)
The datapath control outputs should be given meaningful unique names.

## Slide 35
Soda Dispenser Example
W
ait
Disp
Init
d:='0'
tot:=0
c’*(tot<s)’
c'
*
(
tot<s
)
d:='1'
c
tot:=tot+a
Add
c: bit input, 1 when coin deposited
a: 8-bit input having value of deposited coin
s: 8-bit input having cost of a soda
d: bit output, processor sets to 1 when total value of deposited coins equals or exceeds cost of a soda
Inputs-Outputs
a
s
c
d
Soda
dispenser
processor

## Slide 36
Soda Dispenser Example
Step 2A: Create a datapath
  A register to store item tot
  A comparator to compute tot<s
  An adder to compute tot+a
8
8
8
s
8
a
Datapath
tot_ld
tot_clr
tot_lt_s
ld
clr
tot
8-bit
<
8-bit
adder

## Slide 37
Soda Dispenser Example
Step 2B: Connect the datapath to a controller
  Careful: All inputs and outputs of the controller are one bit signals

## Slide 38
Soda Dispenser Example
Step 2C: Derive an FSM from the HLSM for the controller
  FSM has the same states and transitions as the HLSM
  Implement FSM as a register and combinational logic
W
ait
Disp
Init
d:='0'
tot:=0
c’*(tot<s)’
c'
*
(
tot<s
)
d:='1'
c
tot:=tot+a
Add
tot_ld
tot_clr
tot_lt_s
c
d

## Slide 39
Soda Dispenser Example
d=S1S0
tot_ld=S1
tot_clr=
S1’= +c
S0’=+ + S1
S0’+
Next state – output logic functions
 | Current State |  | Inputs |  | Next State | 
 | S1 | S0 | c | tot_lt_s | S1’ | S0’
Init | 0 | 0 | 0 | 0 | 0 | 1
 | 0 | 0 | 0 | 1 | 0 | 1
 | 0 | 0 | 1 | 0 | 0 | 1
 | 0 | 0 | 1 | 1 | 0 | 1
Wait | 0 | 1 | 0 | 0 | 1 | 1
 | 0 | 1 | 0 | 1 | 0 | 1
 | 0 | 1 | 1 | 0 | 1 | 0
 | 0 | 1 | 1 | 1 | 1 | 0
Add | 1 | 0 | 0 | 0 | 0 | 1
 | 1 | 0 | 0 | 1 | 0 | 1
 | 1 | 0 | 1 | 0 | 0 | 1
 | 1 | 0 | 1 | 1 | 0 | 1
Disp | 1 | 1 | 0 | 0 | 0 | 0
 | 1 | 1 | 0 | 1 | 0 | 0
 | 1 | 1 | 1 | 0 | 0 | 0
 | 1 | 1 | 1 | 1 | 0 | 0
Current State |  | Outputs |  | 
S1 | S0 | d | tot_ld | tot_clr
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
8
8
8
s
8
a
Datapath
tot_ld
tot_clr
tot_lt_s
ld
clr
tot
8-bit
<
8-bit
adder

## Slide 40
Soda Dispenser Example
d=S1S0
tot_ld=S1
tot_clr=
S1’= +c
S0’=+ + S1
S0’+
Next state – output logic functions

## Slide 41: Example: Soda Dispenser
Quick overview example. More details of each step to come.
Inputs
:
c
(bit),
a (8 bits), s (8 bits)
Outputs
:
d (bit) // '1' dispenses soda
Local stor
a
g
e
:
tot (8 bits)
W
ait
Disp
Init
d:='0'
tot:=0
c’*(tot<s)’
c'
*
(
tot<s
)
d:='1'
c
tot:=tot+a
SodaDispenser
Step 1
Step 2A
8
8
8
s
8
a
Datapath
tot_ld
tot_clr
tot_lt_s
ld
clr
tot
8-bit
<
8-bit
adder
Step 2B
a
a
Add

## Slide 42: Example: Soda Dispenser
Quick overview example. More details of each step to come.
Step 1
Step 2B
Step 2C
Inputs
:
c,
tot_lt_s
(bit)
Outputs
:
d,
tot_ld
,
tot_clr
(bit)
Wait
Disp
Init
d=0
tot_clr=1
c'
*
tot_lt_s’
c
¢
*
tot_lt_s
d=1
c
tot_ld=1
c
d
tot_ld
tot_clr
tot_lt_s
Controller
Add

## Slide 43: Example: Soda Dispenser
Quick overview example. More details of each step to come.
Step 2C
Inputs
:
c,
tot_lt_s
(bit)
Outputs
:
d,
tot_ld
,
tot_clr
(bit)
Wait
Disp
Init
d=0
tot_clr=1
c
¢
*
tot_lt_s
¢
c
¢
*
tot_lt_s
d=1
c
tot_ld=1
c
d
tot_ld
tot_clr
tot_lt_s
Controller
Add
Use controller design process (Ch3) to complete the design
a

## Slide 44
High-Level State Machines (HLSMs)
RTL Design Process
  Capture the behaviour using a HLSM
  Convert HLSM to a circuit
    Capture a high-level state machine
    Create a datapath
    Connect the datapath to a controller
    Derive the controller's FSM
Controller-Datapath

## Slide 45
RTL Design Process
RTL design follows two-step process
  Capture the behaviour using a HLSM
  Convert HLSM to a circuit
HLSM is converted to a circuit by using standard processor architecture
External data
outputs
External
control
inputs
Controller
...
External
control
outputs
...
Datapath
...
DP
control
inputs
DP
control
outputs
...
...
...
External data
inputs
Data path has the ability to carry out each data operation in HLSM
Controller sets the control signals for data path components for performing specific actions of each state and to transition to next states

## Slide 46
Creating Datapath
Make all data inputs and outputs to be datapath inputs and outputs
Instantiate (add) a register into the datapath for every local storage item in HLSM
Examine each state action and each transition condition for data computations
Connect components to implement each data computation
Add multiplexers in front of component inputs if necessary
Instance: Instantiated componenet – new component. Give a unique, meaningful name for each component (Reg1, Reg2, TemperatureReg, SensorReg etc.)
A library can be used for component selection during datapath design.

## Slide 47
Creating Datapath
When instantiating a new component for datapath in HLSM all control inputs (like clr, ld, etc.) must be introduced externally.
Unique names must be given to each new component (similar to naming variables in C) such as (Preg_clr, Preg_ld, RegQ_clr, RegQ_ld etc.)
The datapath control outputs should be given meaningful unique names.

## Slide 48: RTL Design Process—Step 2A: Create a datapath
Sub-steps
  HLSM data inputs/outputs  Datapath inputs/outputs.
  HLSM local storage item  Instantiated register
    "Instantiate": Add new component ("instance") to design
  Each HLSM state action and transition condition data computation  Datapath components and connections
    Also instantiate multiplexors as needed
Need component library from which to choose
A
B
S
add
reg
Q
I
ld
clr
A
B
lt
cmp
eq
gt
mux2x1
Q
I
1
s0
I
0
S = A+B
(unsigned)
A<B: lt=1
A=B: eq=1
A>B: gt=1
s0=0: Q=
I
0
s0=1: Q=
I
1
clk^ and clr=1: Q=0
clk^ and ld=1: Q=
I
else Q stays same
shift<L/R>
I
Q
shiftL1: <<1
shiftL2: <<2
shiftR1: >>1
...
Clock rising edge
Clr=ld=1
Clear has priority

## Slide 49: Step 2A: Create a Datapath—Simple Examples
Preg
Q
I
ld
clr
A
B
S
add2
A
B
S
add1
X
Y
Z
(a)
Preg = X + Y + Z
X + Y
X + Y + Z
X
Y
Z
P
0
1
Preg
P
DP
Preg = Preg + X
X
P
Preg
Preg
Q
I
ld
clr
A
B
S
add1
X
(b)
0
1
P
DP
Preg=X+Y; regQ=Y+Z
X
Y
Z
P
Preg
Q
regQ
Preg
Q
I
ld
clr
A
B
S
add2
A
B
S
add1
X
Y
(c)
0
1
P
regQ
Q
I
ld
clr
0
1
Q
Z
DP
k=0: Preg = Y + Z
k=1: Preg = X + Y
X
Y
Z
P
Preg
Preg
Q
I
ld
clr
A
B
S
add2
A
B
S
add1
X
Y
(d)
0
1
P
Z
mux2x1
Q
I
1
s0
I
0
k
k
DP
a

## Slide 50: Example: Laser-Based Distance Measurer
Laser-based distance measurement – pulse laser, measure time T to sense reflection
  Laser light travels at speed of light, 3*108 m/sec
  Distance is thus D = (T sec * 3*108 m/sec) / 2
Object of
interest
D
2D = T sec * 3*108 m/sec
sensor
laser
T (in seconds)
a

## Slide 51
Laser-Based Distance Measurer Example
B: bit input, from button, to begin measurement
L: bit output, activates laser
S: bit input, senses laser reflection
D: 16-bit output, to display computed distance
Inputs-Outputs
S0
S1
S2
S3
L := '0'
Dreg := 0
L := '1'
L := '0'
Dctr := Dctr+1
Dreg := Dctr/2
// calculate D
Dctr := 0
B'
S'
B
S
S4
:
:
DistanceMeasurer

## Slide 52: Laser-Based Distance Measurer—Step 2A: Create a Datapath
HLSM data I/O  DP I/O
HLSM local storage  reg
HLSM state action and transition condition data computation  Datapath components and connections
a
Datapath
Dreg_clr
Dreg_ld
Dctr_clr
Dctr_ld
clr
ld
Q
I
Dreg: reg(16)
A
B
S
Add1: add(16)
clr
ld
Q
Dctr: reg(16)
I
1
16
16
Shr1: shiftR1(16)
I
Q
16
16
16
D

## Slide 53: Laser-Based Distance Measurer—Step 2B: Connecting the Datapath to a Controller
D
B
L
S
16
to display
from button
Controller
to laser
from sensor
Dreg_clr
Dreg_ld
Dctr_clr
Dctr_ld
Datapath
300 MHz Clock
a

## Slide 54: Laser-Based Distance Measurer—Step 2C: Derive the Controller FSM
FSM has same states, transitions, and control I/O
Achieve each HLSM data operation using datapath control signals in FSM
Inputs
:
B, S
Outputs
:
L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_ld
S0
S1
S2
S3
L = 0
L = 1
L = 0
L = 0
B
¢
S
¢
B
S
S4
Dreg_clr = 1
Dreg_l
d
= 0
Dctr_cl
r
= 0
Dctr_ld = 0
(laser off
)
(clear Dreg)
Dreg_clr
= 0
Dreg_ld
= 0
Dctr_clr
= 0
Dctr_ld = 1
(laser off)
(count up)
Dreg_clr = 0
Dreg_ld
= 0
Dctr_clr = 1
Dctr_ld
= 0
(clear count)
L = 0
Dreg_clr
= 0
Dreg_ld
= 1
Dctr_clr
= 0
Dctr_ld = 0
(load Dreg with Dctr/2)
(stop counting)
Dreg_clr = 0
Dreg_ld
= 0
Dctr_clr
= 0
Dctr_ld = 0
(laser on)
Controller
HLSM
a

## Slide 55: Laser-Based Distance Measurer—Step 2C: Derive the Controller FSM
Same FSM, using convention of unassigned outputs implicitly assigned 0
Some assignments to 0 still shown, due to their importance in understanding desired controller behavior

## Slide 56
Laser-Based Distance Measurer Example
STEP 2A
  D becomes the output of datapath
  Every data output is registered
  Dreg is declared for this purpose
  Another register Dctr is instantiated for calculation-local storage
  Control inputs for registers Dreg_clr, Dreg_ld, Dctr_clr, Dctr_ld
  To perform the operation on S3 a 16 bit adder is used.
  To perform the operation on S4 a right shift register is needed (divide by 2)
Datapath
Dreg_clr
Dreg_ld
Dctr_clr
Dctr_ld
clr
ld
Q
I
Dreg: reg(16)
A
B
S
Add1: add(16)
clr
ld
Q
Dctr: reg(16)
I
1
16
16
Shr1: shiftR1(16)
I
Q
16
16
16
D
S0
S1
S2
S3
L := '0'
Dreg := 0
L := '1'
L := '0'
Dctr := Dctr+1
Dreg := Dctr/2
// calculate D
Dctr := 0
B'
S'
B
S
S4
:
:
DistanceMeasurer

## Slide 57
Laser-Based Distance Measurer Example
STEP 2B: Connecting datapath to controller
D
B
L
S
16
to display
from button
Controller
to laser
from sensor
Dreg_clr
Dreg_ld
Dctr_clr
Dctr_ld
Datapath
300 MHz Clock
a

## Slide 58
Laser-Based Distance Measurer Example
STEP 2C: FSM will have the same states and transitions as the HLSM. Controllers inputs and outputs will be single bit.
Inputs
:
B, S
Outputs
:
L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_ld
S0
S1
S2
S3
L = 0
L = 1
L = 0
L = 0
B
¢
S
¢
B
S
S4
Dreg_clr = 1
Dreg_l
d
= 0
Dctr_cl
r
= 0
Dctr_ld = 0
(laser off
)
(clear Dreg)
Dreg_clr
= 0
Dreg_ld
= 0
Dctr_clr
= 0
Dctr_ld = 1
(laser off)
(count up)
Dreg_clr = 0
Dreg_ld
= 0
Dctr_clr = 1
Dctr_ld
= 0
(clear count)
L = 0
Dreg_clr
= 0
Dreg_ld
= 1
Dctr_clr
= 0
Dctr_ld = 0
(load Dreg with Dctr/2)
(stop counting)
Dreg_clr = 0
Dreg_ld
= 0
Dctr_clr
= 0
Dctr_ld = 0
(laser on)
Controller

## Slide 59
Laser-Based Distance Measurer Example
STEP 2C: Complete the RTL design by implementing the FSM using register and combinational logic.
Current State |  |  | Inputs |  | Next State |  | 
S2 | S1 | S0 | B | S | P2' | P1' | P0'
0 | 0 | 0 | X | X | 0 | 0 | 1
0 | 0 | 1 | 0 | X | 0 | 0 | 1
0 | 0 | 1 | 1 | X | 0 | 1 | 0
0 | 1 | 0 | X | X | 0 | 1 | 1
0 | 1 | 1 | X | 0 | 0 | 1 | 1
0 | 1 | 1 | X | 1 | 1 | 0 | 0
1 | 0 | 0 | X | X | 0 | 0 | 1
Current State |  |  | Outputs |  |  |  | 
 |  |  |  | Dreg |  | Dctr | 
S2 | S1 | S0 | L | clr | ld | clr | ld
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
L=
Dreg_clr=
Dreg_ld= S2
Dctr_clr=
Dctr_ld=
tot_clr=
S2’=
S1’=+ +
S0’ + + +S2
Next state – output logic functions

## Slide 60
Laser-Based Distance Measurer Example
STEP 2C: Complete the RTL design by implementing the FSM using register and combinational logic.
Next State Logic
S2’=
S1’=+ +
S0’ + + +S2
S2’
S1’
S0’
S2
S1
S0
Output Logic
L= (S2) ̅S1(S0) ̅
Dreg_clr=(S2) ̅ (S1) ̅ (S0) ̅
Dreg_ld= S2 (S1) ̅ (S0) ̅
Dctr_clr= (S2) ̅ (S1) ̅ S0
Dctr_ld=(S2) ̅ S1 S0
tot_clr= (𝑆1) ̅ (𝑆0) ̅
B
S
S0
S1
S2

## Slide 61
More RTL Design
The datapath library can be extended (subtractor, multiplier, absolute value, up-counter, down-counter, register file, etc.)
Clr signal has priority on the register components
Array is an ordered list of items in HLSM
Ex: List of four 8-bit members can be defined in HLSM as local storage A[4] (8-bit)
Array items can be accessed using the notation A[i]. If a HLSM executes the action A[0]:=2, A[1]:=4, A[2]:=9, A[3]:=12 then the array content will be <2,4,9,12>
HLSM’s inputs, outputs or local storage items can be arrays
During the RTL design, an array can be implemented by using a register file or a memory component in datapath.

## Slide 62: RTL Design Involving Register File or Memory
HLSM array: Ordered list of items
  Ex: Local storage: A[4](8-bit) – 4 8-bit items
  Accessed using notation "A[i]", i is index
  A[0] := 9; A[1] := 8; A[2] := 7; A[3] := 22
    Array contents now: <9, 8, 7, 22>
    X := A[1] will set X to 8
    Note: First element's index is 0
Array can be mapped to instantiated register file or memory

## Slide 63: More RTL Design
Additional datapath components
5.4

## Slide 64
Array Example
Create a HLSM that declares an array A with four 11-bit words. Initialize A[0] to 9, then initialize A[1] to 12, then if A[0]==8, output the content of A[1] on an 11-bit output P, otherwise repeat the initialization.
(a)
Init1
Init2
Out1
A[0] := 9
Preg := A[1]
ArrayEx
Inputs
:
(none)
Outputs
:
P (11 bits)
Local storage
: A[4](11 bits)
A[1] := 12
A[0] == 8
(A[0] == 8)'
Preg := 0
Preg (11 bits)

## Slide 65: Simple Array Example
Preg
Q
I
ld
clr
P
Preg_clr
Preg_ld
DP
(b)
11
A
RF[4](11)
R_d
W_e
W_a
W_d
R_e
R_a
Amux
Q
I
1
s0
I
0
9
12
A_Wa0
A_Wa1
A_We
A_Ra0
A_Ra1
A_Re
A_s
11
11
A
B
lt
Acmp
eq
gt
8
A_eq_8
Controller
(c)
Init1
Init2
Out1
A_s = 0
A_Wa1=0, A_Wa1=0
A_We = 1
Preg_ld = 1
ArrayEx
Inputs
:
A_eq_8
Outputs
:
A_s, A_Wa0, ...
A_s = 1
A_Wa1=0, A_Wa0=1
A_We = 1
A_eq_8
(A_eq_8)'
Preg_clr = 1
A_Ra1=0, A_Ra0=0
A_Re = 1
(a)
Init1
Init2
Out1
A[0] := 9
Preg := A[1]
ArrayEx
Inputs
:
(none)
Outputs
:
P (11 bits)
Local storage
: A[4](11 bits)
A[1] := 12
A[0] == 8
(A[0] == 8)'
Preg := 0
Preg (11 bits)
a
a

## Slide 66
Example
S0
go`
reset
Sreg := 0
sum := 0
P := `1`
S1
P := `0`
S2
go
sum := A+B
S3
sum := sum+C
S4
Sreg := sum
sum < 5099
(sum < 5099)`
For the HLSM given
  Create a datapath

## Slide 67
Example

## Slide 68
RTL Example: Video Compression – Sum of Absolute Differences
Digitized video consist of digitized pictures known as frames. Each pixel of a frame is stored in several bytes. (a frame may require 1 Mbyte data (~720-480, 24 bit depth), for a video with 30fps than 30 Mbytes/sec is needed. Than for one hour video 3600*30=108Gbytes data is needed. This data is huge for downloading or storing.
We need to compress such files or streams
A method is to determine whether successive frames are similar or not
Instead of sending the whole frame every time, we can send a base frame, following data describing just the changing pixels between the base frame and the next frame.
If the difference between two successive frames is much than the difference method will not be feasible.
One way of finding the similarity between the frames is to compute the Sum of Absolute Differences.(SAD)

## Slide 69: RTL Example: Video Compression – Sum of Absolute Differences
Video is a series of frames (e.g., 30 per second)
Most frames similar to previous frame
  Compression idea: just send difference from previous frame
Digitized
frame 2
1 Mbyte
Frame 2
Digitized
frame 1
Frame 1
1 Mbyte
(
a
)
Digitized
frame 1
Frame 1
1 Mbyte
(
b
)
Only difference: ball moving
a
Difference of
2 from 1
0.01 Mbyte
Frame 2
Just send difference

## Slide 70
RTL Example: Video Compression – Sum of Absolute Differences
SAD computes the difference between a pixel value in frame 1 and the value of corresponding pixel in frame 2. (abs(pixel value1-pixel value2))
White pixel = 255, black pixel = 0 then the absolute value of the difference will be 255
Summing these differences for all pixels will result in a number indicating the similarity of two frames.
If the sum is 0, than frames are identical.
If the sum is smaller than a threshold level than we can apply the difference method.
If we could use the difference method than for 10 successive frames than we will save approximately 9 Mbytes.
Instead of comparing all the pixels, pixels can be grouped by 16x16 and comparison can be made in group of pixels

## Slide 71: RTL Example: Video Compression – Sum of Absolute Differences
Need to quickly determine whether two frames are similar enough to just send difference for second frame
  Compare corresponding 16x16 “blocks”
    Treat 16x16 block as 256-byte array
  Compute the absolute value of the difference of each array item
  Sum those differences – if above a threshold, send complete frame for second frame; if below, can use difference method (using another technique, not described)
Frame 2
Frame 1
compare
Each is a pixel, assume represented as 1 byte
(actually, a color picture might have 3 bytes per pixel, for intensity of red, green, and blue components of pixel)

## Slide 72: Array Example: Video Compression—Sum-of-Absolute Differences
a
!go
(i<256)’
S0
S1
S2
S3
S4
go
sum := 0
i := 0
i<256
sum:=sum+abs(A[i]-B[i])
i := i + 1
sadreg := sum
(
b
)
Inputs
: A, B [256](8 bits); go (bit)
Outputs
: sad (32 bits)
Local storage
: sum, sadreg (32 bits); i (9 bits)
A
RF[256](8)
go
SAD
sad
B
RF[256](8)
S0: wait for go
S1: initialize sum and index
S2: check if done ( (i<256)’ )
S3: add difference to sum, increment index
S4: done, write to output sad_reg

## Slide 73: Array Example: Video Compression—Sum-of-Absolute Differences
S0
S1
S2
S3
S4
go
¢
go
go
AB_rd
sum=0 sum_clr=1
i=0 i_clr=1
i<256 i_lt_256
(i<256)’ (i_lt_256)
sum=sum+abs(A[i]-B[i])
sum_ld=1; AB_rd=1
i=i+1 i_inc=1
sad_reg = sum
sadreg_ld=1
Controller
a
i_lt_256
i_inc
i_clr
sum_ld
sum_clr
sadreg_ld
Datapath
sum
sadreg
sad
AB_addr
A_data
B_data
cmp
9
32
8
8
8
8
32
32
32
i
–
+
abs
sadreg_clr
lt
256
A
B
A
B

## Slide 74
RTL Design Process (steps)
  Capture a high-level state machine
  Create a datapath
  Connect the datapath to a controller
  Derive the controller's FSM
Examples

## Slide 75: Array Example: Video Compression—Sum-of-Absolute Differences
S0
S1
S2
S3
S4
go
¢
go
go
AB_rd
sum=0 sum_clr=1
i=0 i_clr=1
i<256 i_lt_256
(i<256)’ (i_lt_256)
sum=sum+abs(A[i]-B[i])
sum_ld=1; AB_rd=1
i=i+1 i_inc=1
sad_reg = sum
sadreg_ld=1
Controller
a
i_lt_256
i_inc
i_clr
sum_ld
sum_clr
sadreg_ld
Datapath
sum
sadreg
sad
AB_addr
A_data
B_data
cmp
9
32
8
8
8
8
32
32
32
i
–
+
abs
sadreg_clr
lt
256
A
B
A
B

## Slide 76: Circuit vs. Microprocessor
Circuit: Two states (S2 & S3) for each i, 256 i’s 512 clock cycles
Microprocessor: Loop (for i = 1 to 256), but for each i, must move memory to local registers, subtract, compute absolute value, add to sum, increment i – say 6 cycles per array item  256*6 = 1536 cycles
Circuit is about 3 times (300%) faster (assuming equal cycle lengths)
Later, we’ll see how to build SAD circuit that is much faster
S3
sum:=sum+abs(A[i]-B[i])
i:=i+1
S2
i<256
(i<256)’
CLR A
MOV R7,A
?C0001:
CLR C
MOV A,#080H
SUBB A,#081H
JNC ?C0004
; A[i] = 0;
; SOURCE LINE # 10
MOV A,#LOW (A?)
ADD A,R7
MOV DPL,A
CLR A
ADDC A,#HIGH (A?)
MOV DPH,A
CLR A
MOVX @DPTR,A
INC R7
SJMP ?C0001

## Slide 77: Common RTL Design Pitfall Involving Storage Updates
Questions
  Value of Q after state A?
  Final state is C or D?
Answers
  Q is NOT 99 after state A
  Q is 99 in state B, so final state is C
  Storage update actions in state occur simultaneously on next clock edge
    Thus, order actions are written is irrelevant
    A's actions same if:
      Q:=R R:=99 or
      R:=99 Q:=R
A
B
C
D
(R<100)'
R<100
R:=R+1
R:=99
Q:=R
Local storage
: R, Q (8 bits)
?
?
99
A
99
?
100
B
100
?
C
R<100
clk
R
Q
a

## Slide 78: Common RTL Design Pitfall Involving Storage Updates
New HLSM using extra state so read of R occurs after write of R
B
A
B2
C
D
(R<100)'
R<100
R:=R+1
Q:=R
R:=99
Q:=R
?
?
99
A
99
?
100
B
100
100
99
99
B2
D
R<100
(R<100)'
clk
R
Q
Local storage
: R, Q (8 bits)

## Slide 79: RTL Design Involving a Timer
Commonly need explicit time intervals
  Ex: Repeatedly blink LED on 1 second, off 1 second
Pre-instantiate timer that HLSM can then use
Init
L:='0'
T:=1000000
T_en:='0'
Timer:
T
Outputs
: L (bit)
BlinkLed
Off
L:='0'
T_en:='1'
T_Q'
On
L:='1'
T_en:='1'
T_Q'
T_Q
T_Q
(b)
load
enable
Q
32-bit
1-microsec
timer T
32
M
T_ld
T_en
T_Q
T_M
BlinkLed
L
(a)
Pre-instantiated timer
HLSM making use of timer
L
a
a

## Slide 80: Button Debouncing
Press button
  Ideally, output changes to 1
  Actually, output bounces
    Due to mechanical reasons
    Like ball bouncing when dropped to floor
Digital circuit can convert actual signal closer to ideal signal
a
B
0
1
button
Ideal:
B
B
B
Actual:
bounce

## Slide 81: Determining Clock Frequency
Designers of digital circuits often want fastest performance
  Means want high clock frequency
Frequency limited by longest register-to-register delay
  Known as critical path
  If clock is any faster, incorrect data may be stored into register
  Longest path on right is 2 ns
    Ignoring wire delays, and register setup and hold times, for simplicity
5.5
a
+
b
c
2 ns
del
a
y
clk

## Slide 82: Critical Path
Example shows four paths
  a to c through +: 2 ns
  a to d through + and *: 7 ns
  b to d through + and *: 7 ns
  b to d through *: 5 ns
Longest path is thus 7 ns
Fastest frequency
  1 / 7 ns = 142 MHz
a
+
*
c
d
5 ns
del
a
y
2 ns
del
a
y
Max
(2,7,7,5)
= 7 ns
a
b
2 ns
5 ns
7 ns
7 ns

## Slide 83: Critical Path Considering Wire Delays
Real wires have delay too
  Must include in critical path
Example shows two paths
  Each is 0.5 + 2 + 0.5 = 3 ns
Trend
  1980s/1990s: Wire delays were tiny compared to logic delays
  But wire delays not shrinking as fast as logic delays
    Wire delays may even be greater than logic delays!
Must also consider register setup and hold times, also add to path
Then add some time to the computed path, just to be safe
  e.g., if path is 3 ns, say 4 ns instead
a
a
+
b
c
2 ns
0.5 ns
0.5 ns
0.5 ns
clk
3 ns
3 ns

## Slide 84: A Circuit May Have Numerous Paths
Paths can exist
  In the datapath
  In the controller
  Between the controller and datapath
  May be hundreds or thousands of paths
Timing analysis tools that evaluate all possible paths automatically very helpful
Combinational logic
c
tot_lt_s
clk
n1
d
tot_ld
tot_lt_s
t
ot_clr
s0
s1
n0
State register
s
8
8
8
8
a
ld
clr
tot
Datapath
8-bit
<
8-bit
adder
(
a
)
(
c
)
(
b
)
a

## Slide 85: RAM Example: Digital Sound Recorder
Behavior
  Record: Digitize sound, store as series of 4096 12-bit digital values in RAM
    We’ll use a 4096x16 RAM (12-bit wide RAM not common)
  Play back later
  Common behavior in telephone answering machine, toys, voice recorders
To record, processor should read a-to-d, store read values into successive RAM words
  To play, processor should read successive RAM words and enable d-to-a
wire
spea
k
er
microphone
wire
analog-to-
digital
co
n
v
e
r
ter
digital-to-
analog
co
n
v
e
r
ter
ad_ld
da_ld
Rrw
Ren
Ra
12
16
processor
ad_
b
uf
data
addr
rw
en
4096x16
RAM

## Slide 86: RAM Example: Digital Sound Recorder
RTL design of processor
  Create HLSM
  Begin with the record behavior
  Create local storage a
    Stores current address, ranges from 0 to 4095 (thus need 12 bits)
  Create state machine that counts from 0 to 4095 using a
    For each a
      Read analog-to-digital conv.
        ad_ld:=‘1’, ad_buf:=‘1’
      Write to RAM at address a
        Rareg:=a, Rrw:=‘1’, Ren:=‘1’
ad_ld:=‘1’
ad_buf:=‘1’
Rareg:=a
Rrw:=‘1’
Ren:=‘1’
S
a:=0
a:=a+1
(a<4095)’
a<4095
T
U
Local register:
a, Rareg (12 bits)
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rw
Ren
Ra
12
16
processor
ad_buf
4096x16
RAM
a
Record behavior

## Slide 87: RAM Example: Digital Sound Recorder
  Now create play behavior
  Use local register a again, create state machine that counts from 0 to 4095 again
    For each a
      Read RAM
      Write to digital-to-analog conv.
    Note: Must write d-to-a one cycle after reading RAM, when the read data is available on the data bus
  The record and play state machines would be parts of a larger state machine controlled by signals that determine when to record or play
a
da_ld:=‘1’
ad_buf:=‘0’
Rareg:=a
Rrw=‘0’
Ren=‘1’
V
a:=‘0’
a:=a+1
(a<4095)’
a<4095
W
X
Local register:
a,Rareg (12 bits)
Play behavior
data bus
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rw
Ren
Ra
12
16
processor
ad_buf
4096x16
RAM

## Slide 88: ROM Example: Talking Doll
Doll plays prerecorded message, triggered by vibration
  Message must be stored without power supply  Use a ROM, not a RAM, because ROM is nonvolatile
    And because message will never change, may use a mask-programmed ROM or OTP ROM
  Processor should wait for vibration (v=1), then read words 0 to 4095 from the ROM, writing each to the d-to-a
4096x16 ROM
processor
Ra
16
Ren
da_ld
digital-to-
analog
converter
v
speaker
vibration
sensor
“Hello there!”
“Hello there!” audio divided into 4096 samples, stored
in ROM
“Hello there!”
a

## Slide 89: ROM Example: Talking Doll
HLSM
  Create state machine that waits for v=1, and then counts from 0 to 4095 using a local storage a
  For each a, read ROM, write to digital-to-analog converter
4096x16 ROM
processor
Ra
16
Ren
da_ld
digital-to-
analog
converter
v
S
a:=‘0’
da_ld:=‘1’
a:=a+1
(a<4095)’
a<4095
T
U
R
areg:=a
R
en:=‘1’
Local register:
a, Rareg (12 bits)
v
v’
a

## Slide 90: ROM Example: Digital Telephone Answering Machine Using a Flash Memory
Want to record the outgoing announcement
  When rec=1, record digitized sound in locations 0 to 4095
  When play=1, play those stored sounds to digital-to-analog converter
What type of memory?
  Should store without power supply – ROM, not RAM
  Should be in-system programmable – EEPROM or Flash, not EPROM, OTP ROM, or mask-programmed ROM
  Will always erase entire memory when reprogramming – Flash better than EEPROM
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rrw
Ren
er
bu
Ra
12
16
processor
ad_buf
4096x16 Flash
rec
play
record
microphone
speaker
data
“We’re not home.”
addr
rw
en
erase
busy

## Slide 91: ROM Example: Digital Telephone Answering Machine Using a Flash Memory
HLSM
  Once rec=1, begin erasing flash by setting er=1
  Wait for flash to finish erasing by waiting for bu=0
  Execute loop that sets local register a from 0 to 4095, reading analog-to-digital converter and writing to flash for each a
analog-to-
digital
converter
digital-to-
analog
converter
ad_ld
da_ld
Rrw
Ren
er
bu
Ra
12
16
processor
ad_buf
4096x16 Flash
rec
play
record
microphone
speaker
T
er:=‘0’
bu
bu’
er:=‘1’
r
ec
S
Local register: a, Rareg (13 bits)
(a<4096)’
a<4096
U
V
ad_ld:=‘1’
ad_buf:=‘1’
Rareg:=a
Rrw:=‘1’
Ren:=‘1’
a:=a+1
a:=‘0’
a

## Slide 92
RTL Design Process (steps)
  Capture a high-level state machine
  Create a datapath
  Connect the datapath to a controller
  Derive the controller's FSM
Examples

## Slide 93
5.2 Capture the following system behavior as a HLSM. The system counts the number of events on a single-bit input B and always outputs that number unsigned on a 16-bit output C, which is initially 0. An event is a change from 0 to 1 or from 1 to 0.
Assume the system count rolls over when the maximum value of C is reached.
Example

## Slide 94
Example

## Slide 95
5.5. Create a high-level state machine that initializes a 16x32 register file’s contents to 0s, beginning the initialization when an input rst becomes 1. The register file does not have a clear input; each register must be individually written with a 0. Do not define 16 states; instead, declare a local storage item so that only a few states need to be defined.
Example

## Slide 96
Example

## Slide 97
Example
Create a high-level state machine for a simple data encryption/decryption device. If a bit-input b is 1, the device stores the data from a 32-bit input I as what is known as an offset value. If b is 0 and another bit-input e is 1, then the device “encrypts” its input I by adding the stored offset value to I, and outputs this encrypted value over a 32-bit output J. If instead another bit-input d is 1, the device should “decrypt” the data on I by subtracting the offset value before outputting the decrypted value over J.

## Slide 98
Example

## Slide 99
Example
For the HLSM given
  Create a datapath
ad_ld:=‘1’
ad_buf:=‘1’
Rareg:=a
Rrw:=‘1’
Ren:=‘1’
S
a:=0
a:=a+1
(a<4095)’
a<4095
T
U
Local register:
a, Rareg (12 bits)

## Slide 100: Chapter Summary
  Modern digital design involves creating processor-level components
  High-level state machines
  RTL design process
    1. Capture behavior: Use HLSM
    2. Convert to circuit
      A. Create datapath B. Connect DP to controller C. Derive controller FSM
  More RTL design
    More components, arrays, timers, control vs. data dominated
  Determining fastest clock frequency
    By finding critical path
  Behavioral-level design – C to gates
    By using method to convert C (subset) to high-level state machine
  Memory components (RAM, ROM)
  Queues
  Multiple processors
  Hierarchy: A key concept used throughout Chapters 2-5